## Slide 1: Challenges
Mini challenge

## Slide 2: Mini challenge
This challenge is intended for the student to review the concepts introduced in this week.
Create a node to drive the gazebo simulated robot in a square path of a side length 2 m.
Use the same node to move the real robot in a square of side length 2 m.
The open loop controller must be robust.
  The student must define what is robustness and implement strategies to achieve it with the controller.
The controller must be, auto-tunned
  The user selects the robot's speed for the path (square figure), and the controller must estimate the time required for each movement.
The controller must take perturbation, nonlinearities, and noise into consideration.
Controller
Real Robot /Gazebo Simulation
/puzzlebot_1/base_controller/cmd_vel
ROS Node

## Slide 3: State Machines
Definition
A state machine is a computational model that transitions between predefined states based on inputs or conditions.
Finite State Machines (FSM) - Fixed number of states.
Why use state machines?
  Structured way to control robotic behaviour.
  Ensures modular, scalable, and readable code.

## Slide 4: Tips
Straight
Turn
Count++
Stop
Count = 0
Start
Time<t_straight
Time>=t_straight
Time>=t_turn
Count >=N_turns && Time >=t_turn
Start?
Variables ready? Simulation ready?
Time<t_turn

## Slide 5: Rules
This is challenge not a class. The students are encouraged to research, improve tune explain their algorithms by themselves.
MCR2(Manchester Robotics) Reserves the right to answer a question if it is determined that the questions contains partially or totally an answer.
The students are welcomed to ask only about the theoretical aspect of the classed.
No remote control or any other form of human interaction with the simulator or ROS is allowed (except at the start when launching the files).
It is forbidden to use any other internet libraires with the exception of standard libraires or NumPy.
If in doubt about libraires please ask any teaching assistant.
Improvements to the algorithms are encouraged and may be used as long as the students provide the reasons and a detailed explanation on the improvements.
All the students must be respectful towards each other and abide by the previously defined rules.
Manchester robotics reserves the right to provide any form of grading. Grading and grading methodology are done by the professor in charge of the unit.